ERIC PAULSON

BUILDER CONTRACTOR

All Types of Residential Building and Contracting

### 21 Old Doansburg Rd.  Brewster, NY 10509

# Tel. 914-953-5306   Fax 845-278-7337

# Email yourcontractor@aol.com

PROPOSAL

24 January 2005

xxxxxx  xxxxxx Architect

xxxxxxxxx Mountain Rd.

xxxxxxxxx,xx  xxxxx-xxxx

Project #1104

Reed Master Bath

Last revision 01/04/05

Contractor proposes to furnish labor and materials as indicated;

- Install wood blocking as per plans for installation of bathroom accessories.

- Install ‘pre-slope’ on bath sub-floor in the area to be the shower, prior to the installation by the owner/contractor’s plumber of the waterproof membrane. Once membrane has been installed; supply labor and materials to create a sloped dry pack mortar base in shower floor for the installation of ceramic or porcelain tile.

- Supply and install “Wonder Board” or substitute on shower walls to the height of the tile work as indicated on plans. Wonderboard shall be installed with “Durock”, coated fasteners.

- Install “Wonder Board” over sub-floor on bath floor. Sub-floor and underlying joists shall be sufficient in structure to properly support the installation of the ceramic tile selected by the owner. This structural requirement is not the responsibility of this contractor to determine, and shall be the sole or shared responsibility of the owner/contractor/architect.

- Finish installed drywall. All seams, corners, and joints shall be covered with an imbedded paper, mesh or metal tape or corner, and finished smooth with three coats of taping compound.

- Drywall is to be supplied and installed by others. Installation shall be neat, clean and tight, with no broken areas, all joints, butts and corners shall be made as tight fitting as possible, all fasteners shall be properly countersunk below the face of the sheetrock

- Install owner supplied tile to wall and floor surfaces (including vanity and splash) as indicated by plan. All setting materials to be provided by this contractor. Tile and grout to be supplied by owner.

- Supply and hang paint grade solid core Luan door with recess to accommodate owner provided installation of owner provided mirror. Hinges and levers to be selected and supplied by owner.

- Trim window, door, arch and base with supplied paint grade square edge stock.

- Supply and apply paint to walls and trim. To consist of;

One coat of latex primer over finished drywall.

Two coats of finish paint, to be Benjamin Moore latex Flat or Eggshell finish on walls and ceilings, two coats Benjamin Moore Satin or Semi Gloss on trim. Color selection is limited to whites and off whites!!!  That means no colors!!!

This contractor proposes to complete the above described work, with the terms imposed for the amount of $18,095.00 (eighteen thousand, ninety five dollars)

Upon acceptance of this proposal, owner or agent shall return to this contractor a signed copy of this proposal with a deposit check in the amount of $1800.00 thus indicating acceptance of the specifications and terms contained with in.

This proposal may be withdrawn if not accepted within thirty days.

Sign here to indicate acceptance of proposal: ___________________________________

Date: ___________________________________

ERIC PAULSON

BUILDER CONTRACTOR

All Types of Residential Building and Contracting

### 21 Old Doansburg Rd.  Brewster, NY 10509

# Tel. 914-953-5306   Fax 845-278-7337

# Email yourcontractor@aol.com

Jeff,

During my effort to determine the correct method of building and waterproofing the “curb” or the step down detail on Reeds shower; I came across a water proofing membrane that seems quite suitable to this application.

It is manufactured by a company named Schluter. The product is called Kerdi.

I am enclosing some information that I was able to copy from their website(s) for you to consider.

I have also enclosed http addresses to the various Schluter websites so that you can investigate the product as well.

I have ordered a product catalogue and a video from them as well.

schluter.com								Schluter-Systems

schluter.com/english/articles/showersystem.htm			Shower System

schluter.com/english/products/2002/sectionh/part3.htm		video link

As you will see from the information available, this product eliminates the need for pre-slope, and a membrane beneath the mortar base of the shower.

If I were to use this system, it would be only with your ok. My plan would be to install this Kerdi membrane over the entire floor in the toilet area of the bath, being a two layer plywood substrate base for the installation of the owner’s tile. You may wish to direct your attention towards the drain itself, as this is the part of the system that will obviously be apparent after the bathroom is complete.

At the threshold of the door to the vanity area, we could switch up to cbu over plywood, or continue throughout with the two layer plywood and the Kerdi membrane.

There remains an issue still of the unfinished edge of the floor tile being exposed at the step down of the shower. Shluter makes a stainless steel round over edging for this application that you may wish to consider.

I do not have pricing on any of these products. If I was to use these products it would eliminate the purchase of some of the cbu for the floor, but additional plywood would still need to be purchased and installed. The use of this Kerdi may create and increase to the price of this proposal. I will not know that until I am able to verify its cost and availability.

If we should decide to not use this product, it will put me back to square one in regards to the proper construction and waterproofing of the shower step. I have invested a considerable amount of time looking into this, and this seems to be the best, if not only solution I have found. I would need to be supplied with written specifications and drawings of any other method of detailing this step.

Sincerely,

Eric Paulson