Minimum Service Calculation

135 Bedford

Building:  Single Family Detached – Rancher, Walkout Basement (unfinished), Attached Garage, Bonus Room (unfinished no access)

Size:  Main – 173m2, Basement –162m2 , Garage – 66m2 , Bonus Room – 28m2

Adjusted Size For Calculation: 173m2 + 66m2 + 28m2 + (162m2 x 75%) = 388.5m2

Basic Load Calculation:  388.5m2 / 90m2 = 4.3 round up to 5

First 90m2	5kw

Second 90m2	1kw

Third 90m2	1kw

Fourth 90m2	1kw

Fifth 90m2	1kw

Basic Total	9kw

Dual Fuel 3.6kw Range: 			6kw (Sized to accomodate12kw range)

Electric 5.15kw Dryer:  5.15kw x 25% =	1.3kw

Heat mats in bathrooms: 10.4m2 x 110w/m2=1.2kw (May not be installed)

Heat mats for deck:  20m2 x 110w/m2 =	2.2kw (May not be installed)

Total Power:				19.7kw

Total Current @ 240v: 				82A

Service Size to be installed:			200A