Here is what the National Estimator Cost book looks like

2 x 4 Studs for 8' Tall Walls8' tall walls, 2 x 4 studs

__________________________________________________________________________

Craft@Hrs	Unit	Material	Labor	Equip.	Total

__________________________________________________________________________

2 x 4 studs for 8' tall walls  Includes white wood studs, nails, southern yellow pine top plate(s) and pressure treated sole plate. Add the cost of anchor bolts, shot fasteners, blocking and tie-downs. Plate material includes 10 % waste. Equipment includes a pneumatic nailer and an 8-1/4" circular saw. Prices per square foot of wall and per linear foot of wall measured on one side.

Craft@Hrs	Unit	Material	Labor	Equipment	Total

__________________________________________________________________________

8' tall walls using lumber at these costs

__________________________________________________________________________

Using lumber at these costs

White wood 2" x 4" x 8’ studs	--@.000	Ea	2.52	--	--	2.52

Southern yellow pine 2" x 4" x 16’	--@.000	Ea	7.34	--	--	7.34

Pressure-treated sole plate 2" x 4" x 16’	--@.000	Ea	10.09	--	--	10.09

8' tall walls, 2 x 4 studs, 12" on center

__________________________________________________________________________

2 x 4 studs, 12" on center

2 plates, hand nailed	B1@.026	SF	0.54	0.63	--	1.17

2 plates, machine nailed	B1@.016	SF	0.54	0.39	0.02	0.95

3 plates, hand nailed	B1@.028	SF	0.59	0.68	--	1.27

3 plates, machine nailed	B1@.017	SF	0.59	0.41	0.02	1.02

8' tall walls, 2 x 4 studs, 12" on center

__________________________________________________________________________

2 x 4 studs, 12" on center

2 plates, hand nailed	B1@.208	LF	4.28	5.05	--	9.33

2 plates, machine nailed	B1@.128	LF	4.28	3.11	0.20	7.59

3 plates, hand nailed	B1@.224	LF	4.70	5.44	--	10.14

3 plates, machine nailed	B1@.136	LF	4.70	3.30	0.20	8.20

8' tall walls, 2 x 4 studs, 16" on center

__________________________________________________________________________

2 x 4 studs, 16" on center

2 plates, hand nailed	B1@.020	SF	0.44	0.49	--	0.93

2 plates, machine nailed	B1@.012	SF	0.44	0.29	0.01	0.74

3 plates, hand nailed	B1@.023	SF	0.50	0.56	--	1.06

3 plates, machine nailed	B1@.014	SF	0.50	0.34	0.01	0.85

8' tall walls, 2 x 4 studs, 16" on center

__________________________________________________________________________

2 x 4 studs, 16" on center

2 plates, hand nailed	B1@.160	LF	3.51	3.89	--	7.39

2 plates, machine nailed	B1@.096	LF	3.51	2.33	0.10	5.94

3 plates, hand nailed	B1@.184	LF	4.03	4.47	--	8.50

3 plates, machine nailed	B1@.112	LF	4.03	2.72	0.10	6.85

Patch hole in drywall

__________________________________________________________________________

Craft@Hrs	Unit	Material	Labor	Total

__________________________________________________________________________

Regular core drywall

__________________________________________________________________________

Regular core drywall. Tapered edges. Cut ends. Labor includes cutting board around electrical boxes and obstacles, installing on wall studs or ceiling joists 8' to 12' above floor level, joint tape, three coats of joint compound and finish sanding. Material includes 1/2 gallon of premixed joint compound per 100 square feet, 38 linear feet of 2" perforated joint tape per 100 square feet, 1/2 pound of drywall screws per 100 square feet and 10% waste.

3/8" x 4' x 8', ceilings	D1@.023	SF	0.25	0.59	0.84

3/8" x 4' x 8', walls	D1@.017	SF	0.25	0.44	0.69

1/2" x 4' x 8', ceilings	D1@.024	SF	0.25	0.61	0.87

1/2" x 4' x 8', walls	D1@.018	SF	0.25	0.46	0.72

1/2" x 4' x 9', ceilings	D1@.024	SF	0.25	0.61	0.87

1/2" x 4' x 9', walls	D1@.018	SF	0.25	0.46	0.72

1/2" x 4' x 10', ceilings	D1@.024	SF	0.25	0.61	0.87

1/2" x 4' x 10', walls	D1@.018	SF	0.25	0.46	0.72

1/2" x 4' x 12', ceilings	D1@.024	SF	0.25	0.61	0.86

1/2" x 4' x 12', walls	D1@.018	SF	0.25	0.46	0.72

1/2" x 54" x 12', ceilings	D1@.024	SF	0.27	0.61	0.89

1/2" x 54" x 12', walls	D1@.018	SF	0.27	0.46	0.74

Craft@Hrs	Unit	Material	Labor	Total

__________________________________________________________________________

1/2" x 4' x 12', ceilings, sag resistant	D1@.024	SF	0.25	0.61	0.86

1/2" x 4' x 12', soffit board	D1@.035	SF	0.32	0.90	1.22

1/2" panels on ceilings, no tape or finish	D1@.012	SF	0.26	0.31	0.57

1/2" panels on walls, no tape or finish	D1@.008	SF	0.26	0.21	0.47

Arches, soffits, recesses, columns, angles	D1@.035	SF	--	0.90	0.90

Firecode type X drywall

__________________________________________________________________________

Firecode type X drywall. Fire-resistant gypsum core. Labor Includes cutting board around electrical boxes and obstacles, installing on wall studs or ceiling joists 8' to 12' above floor level, joint tape, three coats of joint compound and finish sanding. Material includes 1/2 gallon of premixed joint compound per 100 square feet, 38 linear feet of 2" perforated joint tape per 100 square feet, 1/2 pound of drywall screws per 100 square feet and 10% waste.

5/8" x 4' x 6', ceilings	D1@.025	SF	0.44	0.64	1.08

5/8" x 4' x 6', walls	D1@.019	SF	0.35	0.49	0.84

5/8" x 4' x 8', ceilings	D1@.025	SF	0.31	0.64	0.95

5/8" x 4' x 8', walls	D1@.019	SF	0.31	0.49	0.80

5/8" x 4' x 9', ceilings	D1@.025	SF	0.29	0.64	0.93

5/8" x 4' x 9', walls	D1@.019	SF	0.29	0.49	0.78

5/8" x 4' x 10', ceilings	D1@.025	SF	0.33	0.64	0.97

5/8" x 4' x 10', walls	D1@.019	SF	0.33	0.49	0.82

5/8" x 4' x 12', ceilings	D1@.025	SF	0.30	0.64	0.94

5/8" x 4' x 12', walls	D1@.019	SF	0.30	0.49	0.79

5/8" panels on ceilings, no tape or finish	D1@.013	SF	0.27	0.33	0.61

5/8" panels on walls, no tape or finish	D1@.009	SF	0.27	0.23	0.50