AirCycler Control

Your new home is equipped with an air circulation device called the AirCycler FR.  The purpose of this device is to bring fresh air into your house, even when the heater or air conditioner system (HVAC) is not running.  The way it works is that it periodically turns on the fan of your HVAC system even when heating or cooling is not needed.  This is important year round but is essential during the spring and fall when your HVAC system may not come on for days based on the mild weather we enjoy here in NC.  Scientific studies have shown that the occupants of homes with readily available fresh air live healthier lives.  Below are the operating instructions for this device.

Setup

The AirCycler is setup using the three keys on the face of the control: Mode key (center), Up key (top), and Down key (bottom).

Operating Mode

Once installation is complete and the AirCycler is properly powered with 24 Vac, the AirCycler will automatically enter Operating Mode. The factory default settings will be active (20 minutes of FAN OFF time followed by 10 minutes of FAN ON). The LCD display will indicate the current fan activity. If the thermostat has activated heating, cooling, or constant fan operation, the display will indicate fan on. Otherwise, the display will indicate that the fan is off and give the number of minutes remaining until the fan is activated by the AirCycler, or that the fan is on and give the number of minutes remaining until the fan is de-activated by the AirCycler.

Menu Mode

Changing the fan’s operation time:
To enter menu mode, press the Mode key. FAN ON will be flashing on the display. Increase or decrease the number of minutes that the AirCycler will operate the fan. The number of minutes can be set between 1 and 199, or, a setting of unlimited un can be selected. The unlimited setting can be useful if you want the AirCycler to operate the fan continuously after the FAN OFF delay has expired following a cooling or heating cycle.

Setting the delay (fan off time):
To set the delay after the last heating, cooling or fan operation press the mode button again.  FAN OFF will flash on the display.  As above, set the number of minutes between 1 and 199, or select un for unlimited operation.

Test Mode

Test Mode is intended for use by trained technicians who are verifying or demonstrating the control operation. Test Mode can be entered while in Menu Mode by pressing and holding the Mode key for six seconds. Once in Test Mode, minutes become seconds, causing the fan off and fan on times to go sixty times faster than normal. The display will indicate TEST. To exit Test Mode and return to normal Operating Mode, turn the AirCycler off by holding the Mode key for two seconds, then press the Mode key once more to turn the AirCycler back on. The AirCycler will exit Test Mode automatically after ten minutes.

Turning the AirCycler off

Although the AirCycler control should generally be turned on to provide the intended function of ventilation air distribution and whole-house mixing for improved indoor air quality and comfort, it may be desirable to turn the AirCycler off during extended vacation periods. While in Operating Mode, the AirCycler may be turned off by pressing and holding the Mode key for two seconds. To turn the AirCycler back on, press the Mode key. While the AirCycler is turned off, all thermostat functions will continue to operate normally.

For more information visit AirCycler’s web site at www.aircycler.com