Framing Notes

June 30, 2008

Lot #: ______________________

General notes:

- Set mudsills in ½” from edge of foundation to make the sheathed house frame the size shown on the plans.

Rough Openings:

- Window openings are framed 1/4” wider and ½” taller than shown on the plans for Silverline 2200 series windows.

- Door R.O. for a Portrait brand door with a 12” transom is 96½” tall which includes ½” for hardwood floor.

- For Silverline sliding doors, the RO is 72½“ x 80½“

Fireplace and TV niche:

- TV niche has a 2x10 header above it.  The niche opening is framed to 48½” wide.  The top of the “hole height” is variable.  The niche bottom is framed 53½” off the rough floor.

- Blocking (deadwood) provisions for sheetrock must be installed inside the niche.

- The fireplace opening is framed to 36 1/4” W   x  33 3/4” T with a ¾” piece of plywood on the floor.  (net height 33”)  This is for Vermont castings 36” electric fireplace.

- The fireplace mantle is ~70” wide so the fireplace framing façade must be framed that wide,

- Fire-block top of chase with ¾” OSB AFTER INSULATION

General:

- Kitchen Knee-walls are a total of  45” tall including 1 top plate.  They are glued to the floor with sub-floor adhesive.  The overall height of the kitchen counter top including the back splash is 40 ½”

- Kitchen window bottom RO must be at least 44” above sub floor.

- All walls are to be installed with lots of subfloor adhesive below the sole plate.

- Stair rake knee-walls are framed flush with the stair skirt board or slightly below.

- The front porch beam is 3 2x10s and is set in 3” from front making the front porch 3” narrower than shown on the plans.  4’ porches are 3’9” and 5’ porches are 4’ 9”, etc.

- Order front and back doors with bead bolt bores.

- Do NOT install button caps right up next to window or door Rough openings.

- Do not put a stud in the center of the oven/cook top as the hood vent duct must go here.

- 5’ Bathtub openings are 60” exactly

Framing checks for punch list (before framers leave):

- Check the size of all window openings.

- Check the size of all door openings.

- Check bathtub openings.

- Plumb all door jack studs.

- On any plan with a girder truss in the roof, be sure it is supported all the way down to the foundation with stud columns.

- For stud columns with > 3 studs, strap with metal in 3 places.  For 3 stud columns, nail on both sides of the column so the inspector can see the nails.

- Pull down attic stair hole is 54½“ x 22½“

- All headers to be tight to jack studs or shimmed.  All headers to be visibly nailed to king studs.

- Check engineering on house for number of jack studs, header sizes, stud columns, etc.

- Fir front porch ceiling with 2x4s 16” on center

- Add blocking inside to first floor sheathing joints where necessary. 3.5” dimension vertical.

- Check drywall nailers inside TV niche.

- Add studs beside where tubs will go.  
    Tub actual size inc flange:	42” tub/shower:	60”w      X      	41”d  	76 ½”

Builder tub/shower:	59¾” w  X	32”d	 75 ¼” t

5’ soaker tub: 		60” w     X     	41½”d   24 ½” t

36”x48” shower:	 48” w    X     	34½”d   73 ½“ t

- Install steps, kneewall(s) etc.

- Cut fascia boards up off of roof.

- Check fireblocking in top of chase(s) (3x4” plywood)

- Add blocking for stair rails were necessary

- Add blocking for cabinets where necessary

- Add blocking for bathroom grab bars if any.

- _________________________________________________________________

- _________________________________________________________________

- _________________________________________________________________

- _________________________________________________________________